## Slide 1: Real-Time Tracking of the intramolecular vibrational dynamics of liquid water
09.03.2026, ELIXIR-2026, Synchrotron Soleil
Oliviero Cannelli

## Slide 2: Ultrafast spectroscopy at extreme time scales
Vibrational delocalization and energy dissipation in water
Phenylalanine
Methyl lactate
F. Calegari et al., Science346.6207 (2014): 336-339.
V. Wanie et al., Nature 630.8015 (2024): 109-115.
Extension to condensed phase
Charge migration
Chiral current driven by electronic coherences
Image by Mischa Flór, EPFL.

## Slide 3: Coherent wavepacket dynamics
Impulsive laser excitation
Coherent modulation of refractive index
ΔE ~ 100 meV
period ~40 fs
nuclear coordinate
ħω
Nuclear wavepacket dynamics
CMOS detector
pump
probe
sample
Δt
nuclear coordinate
ħω
Resonant
excitation
Impulsive stimulated Raman scattering (ISRS)

## Slide 4: Practical requirements for coherent wavepacket spectroscopy
Define relevant time scales:
Generate pulses with appropriate duration
  Pump: established technology in NIR-Vis: hollow core fiber <5 fs
  Probe: possibly non-degenerate, generally UV <2 fs
Preserve temporal duration
  Avoid dispersive materials, reflection geometry (no transmission), avoid air: vacuum
Sample interaction region: vacuum + liquid + thin: liquid jet technology
symmetric stretching
asymmetric stretching
bending
C. Choe, et al. Analyst 141.22 (2016): 6329-6337.
<9 fs
M. Nisoli, et al. Applied Physics Letters 68.20 (1996): 2793-2795.
M. Galli, et al. Optics letters 44.6 (2019): 1308-1311.
J.C. Travers, et al. Nature Photonics 13.8 (2019): 547-554.

## Slide 5: Starlight setup for NIR-Vis-UV-XUV spectroscopy
IR pump
UV probe
Liquid jet

## Slide 6: Liquid jet setup
Chip (5 m to sub-1 m) and catcher
Recycling system
Pressure from 25 mbar to 10-3 mbar and quick venting port
UV detection outside vacuum

## Slide 7: Experimental scheme
ISRS of water
Nuclear wavepacket dynamics
Ultrabroadband UV probe (< 2 fs)
NIR-Vis pump (< 5 fs)

## Slide 8: Real-time water stretching
C. Choe, et al. Analyst 141.22 (2016): 6329-6337.
Coherent oscillation dominated by the O-H stretching mode
Dephasing due to intermolecular coupling
G. Giovannetti, et al. Commun. Chem. 9.57 (2026)

## Slide 9: Antiphase oscillation
Node at 260 nm (and 305 nm)

## Slide 10: Diagrammatic description of ISRS
ISRS: linear superposition of two Feynman diagrams
They involve different probe intensities (shifted from )
Each diagram dominates at tails, but they cancel out in the middle
For non-transform limited pulses the chirp introduces a phase difference
from destructive to constructive interference!
L. Monacelli, et al. JPCL 8.5 (2017): 966-974.

## Slide 11: Chirp-dependence of ISRS
Excellent agreement in modelling the chirp-dependence of the ISRS process
Experiment
Model
G. Giovannetti, et al. Commun. Chem. 9.57 (2026)

## Slide 12: Conclusions and perspectives
Demonstrating real-time tracking of liquid water vibrational dynamics enables extending few-fs wavepacket dynamics in solution phase

## Slide 13: Acknowledgements
Gaia Giovannetti
Sabine Rockenstein
Sergey Ryabchuk
Ammar Bin Wahid
Aurelien Sanchez
Kate Robertson
Kai-Fu Wong
Agata Azzolin
Linda Oberti
Oliviero Cannelli
Erik P. Månsson
Terry Mullins
Andrea Trabattoni
Vincent Wanie
Francesca Calegari
Ofer Neufeld
Angel Rubio
Emanuele Mai
Giovanni Batignani
Tullio Scopigno
Hui-Yuan Chen
Sebastian Jackson
Cristian Soncini
Majed Chergui
Geoffrey Carneiro Gabriele Crippa
Hugo Marroux

## Slide 15: Chirp-dependence and modelling

## Slide 16: ISRS fluence dependence

## Slide 17: Current status fo the liquid jet

## Slide 18: Transient signal at t0

## Slide 20: Generic slide with
Reference
Something
Something else
Question and some text bold

## Slide 21
Understanding the properties of aqueous solutions is a key first step in determining the effects of the liquid environment on the chemical reactions occurring in biological systems. For this reason vibrational relaxation and therefore energy dissipation in liquid water have been intensely investigated [1].
Many of the unique properties of water originate from the hydrogen bond network of water, which results from the strong intermolecular interactions between water molecules. For instance, the water H-bond network allows for rapid delocalization and dissipation of excess energy following chemical reactions, thereby making reactions irreversible.
For water, different O-H stretch modes are known to be very strongly coupled both within and between water molecules, leading to ultrafast dissipation and delocalization of vibrational energy [2].