## Slide 1
BESSY II
status & upgrade
10.30.2025
Meghan McAteer on behalf of the BII machine group
ESLS 2025
SOLEIL

## Slide 2: BESSY II Machine Group
Michael Abo-Bakr, Pauline Ahmels, Rebecca Barsotti, Beñat Alberdi Esuain, Terry Atkinson, Yvonne Bergmann, Thomas Birke, Daniel Böhlick, Jörg Borninkhof, Anne Bundels, Robert Burneleit, Natthawut Chaisueb, Nathalie Childs, Matthias Diehn, Marc Dirsat, Olaf Dreßler, Michael Edling, Silvio Ehlert, Dan Eichel, Volker Dürr, Pablo Echevarria, Dennis Engel, Fjodor Falkenstern, Jörg Feikes, Nadine Fischer, Roland Fleischhauer, Andre Frahm, Benjamin Franksen, Holger Glass, Hans-Walter Glock, Felix Glöckner, Anny Gora, Paul Goslawski, Malte Gotz, Ronja Grünke, Mario Haucke, Jochen Heinrich, Stine Heise, Marco Herzog, Sören Heucke, Andreas Heugel, Frank Hoeft, Harry Hoffmann, Falk Hoffmann, Karsten Holldack, Holger Huck, Karsten Janke, Andreas Jankowiak, Sébastien Joly, Christian Jung, Nicole Kaubisch, Christian Kalus, Jens Knobloch, Jörg Kolbe, Arnold Kruschinski, Bernhard Kuner, Jens Kuszynski, Victoria Laux, Sven Lederer, Benjamin Liebe, Melis Löhr, Tobias Loewner, Michael Markert, Aleksandr Matveenko, Meghan McAteer, Andreas Meissner, Marco Marongiu, Ingo Müller, Nicolas Müller, Christian Nass, Ingo Neumann, Teresia Olsson, Volker Oswald, Sylvia Pavlis, Götz Pfeiffer, Fabian Pflocksch, Lutz Pichl, Henry Plötz, Jens Raeder, Günther Rehm, Markus Ries, Stefan Rotterdam, David Rückert, Roswitha Schabardin, Andreas Schälicke, Tobias Schneegans, Günter Schindhelm, Kevin Schemmel, Gregor Schiwietz, Jörg Schleuer, Pierre Schnizer, Bernhard Schriefer, Christoph Schröder, Michael Schuster, Dirk Schüler, Ines Seiler, Nicola Selbach, Liangliang Shi, Irma Shmidt, Hannes Stein, Tom Struppert, Waheedullah Sulaiman Khail, Ervis Suljoti, Fatbardh Tafaj, Yegor Tamashevich, Michael Ulrich, Stefan Wiese, Daniel Wolk, Adolfo Velez, Marie-Louis Venzke, Jens Völker, Antje Vollmer, Sven Wrede, Anna Ziegler, …
and many more

## Slide 3
BESSY II, Berlin, Germany
Parameters | 
Energy | 
Circumference | 
Horizontal emittance | 
Beam current | 
RF frequency | 
max. RF voltage | 
Bunch length (zero current) low-α | 
Mom. Comp. factor low-α | 
Parameters | 
Energy | 
Circumference | 
Horizontal emittance | 
Beam current | 
RF frequency | 
max. RF voltage | 
Bunch length (zero current) low-α | 
Mom. Comp. factor low-α | 
in user operation since 1998
diverse user community
offering short x-ray pulses and timing
‘New’ fill-pattern (shorter gap, reduced transients, increased lifetime, more efficient bunch lengthening)

## Slide 4: Operation Statistics

## Slide 5
operation schedule for 2025

## Slide 6
Year | Scheduled | Delivered | Downtime | Outages | Availability | MTBF | MTTR
2013 | 4505 h | 4346 h | 159.3 h | 105 | 96.5% | 42.9 h | 1.52 h
2014 | 5408 h | 5024 h | 384.4 h | 136 | 92.9% | 39.8 h | 2.83 h
2015 | 3896 h | 3804 h | 92.5 h | 90 | 97.6% | 43.3 h | 1.03 h
2016 | 4855 h | 4793 h | 61.9 h | 69 | 98.7% | 70.4 h | 0.91 h
2017 | 4299 h | 4050 h | 249.5 h | 62 | 94.2% | 69.3 h | 4.02 h
2018 | 3578 h | 3550 h | 28.3 h | 51 | 99.2% | 70.2 h | 0.56 h
2019 | 4058 h | 3990 h | 67.7 h | 67 | 98.3% | 60.6 h | 1.01 h
2020 | 3455 h | 3404 h | 50.9 h | 49 | 98.5% | 70.5 h | 1.04 h
2021 | 4968 h | 4917 h | 50.6 h | 59 | 99.0% | 84.2 h | 0.86 h
2022 | 3724 h | 3695 h | 29.0 h | 38 | 99.2% | 98.0 h | 0.76 h
2023 | 4587 h | 4528 h | 58.2 h | 48 | 98.7% | 95.6 h | 1.21 h
2024 | 4732 h | 4669 h | 63.4 h | 61 | 98.7% | 77.6 h | 1.04 h
2025* | 3839 h | 3736 h | 103.2 h** | 46 | 97.3% | 76.8 h | 2.06 h
Availability statistics
* Until 2025.10.28

## Slide 7
Availability
Vacuum event

## Slide 8
number of outages
Chart: 
| RF | Control System | Vacuum | Infrastructure | Injector/ LINAC | Interlock Systems | Diagnostics | Others | Unidentified | Pulsed Elements | Insertion Devices | Power Supplies
 | 4 | 1 | 1 | 1 | 6 | 1 | 4 | 2 | 2 | 16 | 4 | 4

## Slide 9
Duration of outages (total = 128H, of which 80h due to vacuum event)
Chart: Duration of outages (hours)
| RF | Control System | Vacuum | Infrastructure | Injector/ LINAC | Interlock Systems | Diagnostics | Others | Unidentified | Pulsed Elements | Insertion Devices | Power Supplies
 | 4.0833 | 4.1 | 79.7333 | 7.05 | 5.2 | 2.9667 | 3.0833 | 0.8 | 1.1 | 6.6833 | 3.7 | 9.15

## Slide 10
Vacuum intervention (March 2025)
Heating and discharges; couldn’t store 200 mA
Happened on Friday before Machine Commissioning week -> quick decision to break vacuum before weekend to investigate
Found mismatched RF connector (bad fit left a gap)
Beam scrubbing the following week

## Slide 11
Other disturbances
Lots of construction work and vibrations (two new buildings, new underground electrical infrastructure)
Two significant power outages
  Five minutes (during user operation – 6 hrs to get beam back)
  Three days (during shutdown)
Network disruption due to failure in server room (luckily no disruption to user operation)

## Slide 12: Recent Developments

## Slide 13
shutdown work 2025
Sections of vacuum chamber replaced
Redesign of magnet feedback loop in Booster dipoles; (attempted) long-term study of magnet stability
Prototype harmonic cavity uninstalled
Extensive surveying campaign
Removal of heating jackets
Much more…

## Slide 14
Replacement of vacuum chamber sections
Last year: intermittent low-frequency mystery noise in vertical beam motion

## Slide 15
Replacement of vacuum chamber sections
Sections of copper vacuum chamber replaced
Burn marks evident on vacuum chamber, photon absorbers

## Slide 16
Startup after shutdown 2025:
Beamscrubbing

## Slide 17
BII perspectives until 2035
Planned upgrades and developments:
  BPM system
  Timing system renovation
  Vacuum system renovation
  Magnet power supply renovation
  1.5 GHz cavities, 1.75 GHz cavities, digital LLRF
  New WLS
  Digital Twin

## Slide 18
  Timing system renovation
  Vacuum system renovation
  Magnet power supply renovation
  1.5 GHz cavities, 1.75 GHz cavities, digital LLRF
  New WLS
  Permanent magnets
  Digital Twin
BII perspectives until 2035
Planned upgrades and developments:
  BPM system
    Phased installation of Libera Sparks (w/ hybrid orbit correction) completed; full TBT capability
    Lots of BBA (of quads and sextupoles)

## Slide 19
BII perspectives until 2035
Planned upgrades and developments:
  BPM system
  Timing system renovation
    First components operational; will continue with phased approach
  Vacuum system renovation
  Magnet power supply renovation
  1.5 GHz cavities, 1.75 GHz cavities, digital LLRF
  New WLS
  Digital Twin

## Slide 20
BII perspectives until 2035
Planned upgrades and developments:
  BPM system
  Timing system renovation
  Vacuum system renovation
  Magnet power supply renovation
    100 power supplies replaced (slicing bends, magnet families in straight sections)
    Phased approach (5 per week)
  1.5 GHz cavities, 1.75 GHz cavities, digital LLRF
  New WLS
  Permanent magnets
  Digital Twin

## Slide 21
BII perspectives until 2035
Planned upgrades and developments:
  BPM system
  Timing system renovation
  Vacuum system renovation
  Magnet power supply renovation
  1.5 GHz cavities, 1.75 GHz cavities, digital LLRF
  New WLS
  Digital Twin

## Slide 22: Higher-harmonic cavities and digital LLRF
1.5 GHz cavities (bunch lengthening):
Prototype EU harmonic cavity of Alba design uninstalled
First new cavity received, conditioning started
Remainder arriving before end of year; installation in 2026
1.75 GHz cavities (variable bunch lengthening):
Installation in 2027
Digital LLRF
Replacing LLRF for all frequencies in all rings
Call for tender completed, delivery of first system expected in November, remainder next year
Phased installation, starting with 1.5 GHz cavities in 2026

## Slide 23
BII perspectives until 2035
Planned upgrades and developments:
  BPM system
  Timing system renovation
  Vacuum system renovation
  Magnet power supply renovation
  1.5 GHz cavities, 1.75 GHz cavities, digital LLRF
  New WLS
  Digital Twin

## Slide 24: 7T wavelength shifter
an established and efficient way to extend the spectral range towards tender x-rays
Existing WLS built by BINP, Novosibirsk, Russia
Maintenance is not available in foreseeable future; reliable but not expected to last until 2035
Replacement project:
Discussions with European manufacturers; call for tender soon
Replicate existing functionality, maybe with design modifications (dry cryostat, smaller vertical gap, maybe 5 SC coils instead of 3)
replacement on site for BESSY II not later than 2029…

## Slide 25
BII perspectives until 2035
Planned upgrades and developments:
  BPM system
  Timing system renovation
  Vacuum system renovation
  Magnet power supply renovation
  1.5 GHz cavities, 1.75 GHz cavities, digital LLRF
  New WLS
  Digital Twin
    Simulated commissioning / preparing scripts
    Details of software architecture:

## Slide 26: BIII Planning

## Slide 27
Slide courtesy of P. Goslawski
BESSY III Baseline lattice
A systematic, deterministic lattice approach
  stepwise investigation of the MBA lattice basic building blocks! Power and Function of each Component & “Knob”  LEGO approach
  with relaxed hardware to minimize the technique risk
  not only focusing on emittance, but also on stability & flexibility  Good control of non-linear beam dynamics
6MB-HOA with homogenous metrology bends
  100 pm rad emittance @ 2.5 GeV, with 16 straights on 350 m
  15µm source size, 10 ps zero current bunch length, lifetime > 5 h
Sustainibility and power consumption
  dipoles and quadrupoles mainly build as permanent magnets
  power consumption reduce from 1000 kW for electro magnets down to < 200 kW

## Slide 28
Slide courtesy of P. Goslawski
BESSY III Baseline lattice
Flexibility of bending dipole sources
  Extract up to two dipol bending beamlines per 6-MBA arc
  The critical photon energy is to some extent adjustable with Longitudinal Gradient Bends (LGBs)
Magnetic Field: 0.64 T 1.5 T 2.5 T
Critical Photon Energy: 2.6 keV 6.2 keV 10.4 keV
εc = 2.50 keV, B = 1.3 T
εc = 13.3 keV, B = 6.9 T
εc = 2.64 keV, B = 1.5 T
εc = 6.23 keV, B = 1.5 T
εc = 10.4 keV, B = 2.5 T
BESSY II
BESSY III

## Slide 29
Slide courtesy of P. Goslawski
BESSY III Baseline lattice
Pushing the lattice toward the TDR phase
  Technical/engineering adaptions: Absorbers, Front-Ends, Syn.Rad. Extraction
  Orbit/Optics etc. Correction Schemes: BPMs, Steerers, etc.
  Injection scheme / Injection optics: Lattice adaption for injection dynamics & hardware: septum and non-linear kicker
  Non-linear optimization to find the operational sweet spot Operation Schemes
  Collective Effects & Bunch Length Manipulation

## Slide 30: Questions? Comments?
photo A. Vollmer