## Slide 1: The ThomX Compton Source
Nicolas DELERUE (IJCLab, Paris-Saclay University)
on behalf of the ThomX collaboration

## Slide 2: Compact Compton Sources
High brightness beam on the laboratory-scale facilities (hospitals, labs, museums…)
Beam is produced in a untypical way
  Compactness (footprint ~ 100 m2)
  Tunable X-ray beam energy
  Large X-ray energy range (keV to MeV)
  High brightness 1011 – 1013 ph/(s.mm2.mrad2) in 0.1% BW
  Flux 1012 - 1013 ph/s
nominal energy flux brightness
ThomX (Orsay, FR) 45-90 keV 1013 ph/s ~ 1011
MuCLS 15-35 keV 1010 - 1011 ph/s 108 - 109
Lync. Tech (Munich, DE)
*Only 2 “high-flux” Compton sources currently in the world
X-rays produced by Compton interaction

## Slide 3: ThomX facility
Compact Compton light source
Thom X
Sir Joseph John Thomson
(1856 –1940)
X-rays

## Slide 4: ThomX : on the Orsay campus
Orsay Campus with Saclay in the back
SOLEIL ~2km
Using the former LURE DCI building

## Slide 5
ThomX facility
ThomX is a demonstrator
& research platform
Compact X-ray source, affordable for museums, hospitals…
Users: cultural heritage, bio-medical and therapy applications, crystallography, X-ray imaging…
ThomX target is a high AVERAGE FLUX ➔ many electrons and laser photons colliding in a small volume at high frequency !
Maximize collision frequency
Maximize electron bunch charge
Maximize laser pulse power
Minimize source size
e- beam
dump
Laser + 4 mirrors FP cavity
X-rays
e- beam
dump
Transfer line (transport & diags.)
Ring
Injector + Linac
Ee = 50 MeV - 70 MeV
45 keV - 90 keV
10 mrad /22 keV - 7 mrad / 45 keV
X-rays energy scales with 𝛄4
7m

## Slide 6: ThomX facility: milestones
Budget : National Research Agency (ANR) /Equipex 12 M€
Installation and operation (2012-2023)
8 French partners :
LAL/IJCLab, SOLEIL, CELIA, LAMS, ESRF, NEEL, INSERM,Thalès
Civil engineering: 2,2 M€
(local Essonne funding)
University Paris-Sud, CNRS/IN2P3,
SESAME, IJCLab : ~ 1 M€

## Slide 7
RING plates alignement
Civil engineering
X-LINE
table
Fabry-Perrot cavity
in BUNKER
RING
X-LINE in X-Hutch
ThomX facility
April 2025

## Slide 8
Laser +
4 mirrors FP cavity
Ring
Injector + Linac
Extraction line (diags.)
Experimental
X-hutch
X-rays
Transfer line
(transport & diags.)
50-70 MeV, 1nC, 50 Hz
Bunker X-line
Ee = 50 MeV - 70 MeV
45 keV - 90 keV
10 mrad /22 keV - 7 mrad / 45 keV
θ (mrad)
EX (keV)
90
45
Ee = 70 MeV
Ee = 50 MeV
10
-10
Electron accelerator
1 nc / bunch @50 Hz
50-70 MeV
Ring, 16 MHz frep
Energy spread < 0.5%
N ~ 5-10 mm.mrad
τe ~ 10-30 ps
σe ≳ 70 μm
Laser /Cavity system
100 W injected average power
> 0.5 MW stored inside the Fabry-Perrot cavity (~ 15 mJ/pulse)
X-ray beam
Flux ~ 1013 ph/s
Brightness ~1011 ph/(s.mm2.mrad2) in 0.1% BW
σx ~ 70 μm
On-axis Energy ~ 45 – 90 keV
ThomX facility: nominal parameters

## Slide 9: ThomX injector
Photocathode RF gun
Accelerating structure
➜ 2.5-cell photocathode RF gun : Ez = 80 MV/m @ 6 MW to reach E = 5 MeV, Charge 0.1/1 nC
LAL design
made in-house
Linac RF
ScandiNova modulator,
3 GHz Toshiba klystron E37310
Standard design of photoinjector + S-band RF structure + Transfer/Extraction Line
Injector specification |  |  | 
Parameter | Nom. value | Measured | Units
Energy | 50/70 | 40, 50, 61.5, 70 | MeV
Charge, commissioning/nom. | 0.1/1 | >0.2 | nC
Nb. of bunches per RF pulse | 1 | 1 | 
Energy spread, rms | <1 | 0.08 | %
Emittance (rms, normalized) | <5 | <5 | mmmrad
Bunch length, rms | <5 | 3.9 | ps
Average current | 50 | 1 | nA
Pulse repetition rate | 50 | 10 | Hz
➜ S-band :4.8-meter long accelerating structure (2998.55 MHz) to reach ~45 MeV @ 11 MW

## Slide 10
Linac, Transfer Line and Extraction Line
6 Dipoles
14 Quadrupoles
2 Dipoles for inj./extr.
8 Correctors
7 BPM
5 Diagnostic stations
3 ICT
2 Faraday Cups
04/08/2023
04/08/2023
04/08/2023
04/08/2023
09/12/2022
System of linear equations for the thick lens approximation is solved c.f. M.C. Ross et al. PAC87
RF-gun
Dump
Dump
To ring
21/03/2025
21/03/2025
21/03/2025
rms = 0.08%
21/03/2025
@ Isol = 230 A,
50 MeV

## Slide 11: Ring lattice and nominal parameters
8 Dipoles
24 Quadrupoles
12 Sextupoles
2 Kickers
1 Septum
1 RF cavity
12 BPM
12 Correctors
Working point 3.17/1.64
28x40 mm
11
ThomX SR: L = 18 m, T = 60 ns, frep = 16.7 MHz
Very dense integration
Parameter | Value/Units
Beam energy | 50-70 MeV
Bunch Charge | 1 nC
Bunch length (rms) | ~30 ps
Circumference | 18 m
Revolution frequency | 16.7 MHz
Current | 16.7 mA
RF frequency/Harmonics | 500/30 MHz
Momentum compaction | 0.0125 - 0.025
Betatron tunes | 3.17/1.64
Natural chromaticity | -9/-13
Damping time trans./long. | 1.2/0.6 s
Repetition frequency | 50 Hz (20 ms)
Beam size at the IP | ≳70 μm
Nominal RF Voltage/cavity | 300 kV (500 kV max)
Energy loss per turn | 1.57 eV
IP
IP

## Slide 12: Ring commissioning highlights
The Ring operation and its commissioning is a big challenge due to :
high particle density (1 nC/bunch) and low energy operation (50-70 MeV)
mismatched beam injection
absence of the synchrotron damping (stored time << damping time)
strong impact of collective effects (intrabeam and Compton scattering, coherent synchrotron radiation, ion instabilities, etc.)
Beam dynamics is very different from usual dynamics in synchrotrons
IBS only
IBS + Compton
Model hor./vert. tune
3.17/1.64
Tune
Improvement in beam storage: @10 Hz ~95 %
Physics model vs. real machine: good.
Work in progress!
X-ray flux drops by 30 %
in ~60 s
1 nC/bunch
≲ 100 pC/bunch
νx = 0.174
νy = 0.646
Orbit
Dispersion
Stored charge

## Slide 13: An unexpected find: shorter circumference
Short and small-radius dipoles
The RF frequency was found to be ~0.4 MHz higher. A big difficulty for synchronization with the Fabry-Perot cavity laser (limited BW, ≤ 0.25 MHz)
To guarantee the high-intensity X-ray production:
mechanical extension of the ring by ~12 mm
☞ shorter pathlength and so smaller total circumference
EXAMPLE
+6mm drifts

## Slide 14: Fabry-Perot cavity @ThomX
Optical table is installed on the hexapode (µm precision)
Oscil. LASER 40 mW, 33.3 MHz, 10-15 ps, 1031 nm
Optical FIBER AMPLIFICATION
(fibers doped with Ytterbium)
 50 - 100 W (1 - 2 μJ/pulse)
Optical CAVITY AMPLIFICATION
4 mirrors planar cavity
2 plan & 2 spherical
Optical path ~ 9 m
Gain 10000
0.5 - 1 MW stored power
Length ~ 10 ps (rms)
Spot size ~ 70 μm (rms)

## Slide 15: X-line design
Experimental
X-hutch
BUNKER
Table 1 (igloo)
Follow the beam line
On-line monitoring of the X-ray beam
BW selection
Collimation et focusing of the X-ray beam (transfocator)
Table 2 (hall D1)
Characterization of the X-rays
Monochromator
Experimental set-ups
Detectors (spectrometers, X-ray cameras, etc.)
X-LINE elements inside bunker
X-LINE in X-Hutch

## Slide 16: The first X-rays
23 June 2023
Laser LOCKED (~25-30 kW stored)
No e- beam
shutter CLOSED
Laser
DELOCKED
Laser
scattering
Background
X-ray
signal
Measured photodiode signal
A few minutes scale
Signal intensity (pA)
25 pA
e-/laser beams
NOT synchronised
520
570
Expected Flux ~ (0.5 - 2)∙107 ph/s
(uncertainty on stored e- bunch charge
and bunch length)
Measured Flux ~107 ph/s
X-ray flux measurement
M. Jacquet et al. "First production of X-rays at the ThomX high-intensity Compton source."
Eur. Phys. J. Plus 139, 459 (2024)

## Slide 17
Current X-ray operational performance
15 cm
Spectrum
ABSOLUTE FLUX measurement in X-Hutch with a calibrated diode
Total FLUX ~ 3  1010 ph/s
Calibrated Si diode
(Canberra)
Spectrometer CdTe
X-rays energy (keV) for electrons at 50 MeV, 61 MeV and 70 MeV
Preliminary Results

## Slide 18: Ring operation highlights
Using/Assumed
Typical operational values for e- beam @IP

e-
Laser beam
long scan duration (many minutes)
☞ good extraction of electron beam size @IP
Measurement of the vertical e- beam size @IP
X-ray detector
(fluo screen + pdiode)
X-rays
From the model and using injector measured emittances
Minimum 𝜎𝑒VERT ≈ 60 – 120 µm (expected)
@IP

## Slide 19
Using/Assumed
 (vert.)
« single shot » online source size measurement:
☞ Electron beam size extraction @IP
☞ X-ray source position estimation
Projections of the edges
source
Slit /edge
Detector plan
Blur due to source size
X-ray beam
Preliminary Results
Data from 18/03/2025
Source size measurement
e- vert. beam size is in good agreement
with other measurements and model

## Slide 20: Two ways to use the Compton beam
 Measure large samples in a single exposure
(patient, materials …)
1. Divergent beam in 2D
Biomedical/cultural heritage applications
Conventional Radiography
K-edge subtraction
Phase contrast imaging
RADIOTHERAPY
IMAGING
• Several cm diameter
• Pink beam (few % - 30% )
2. Beam core
(Cultural heritage, material science, biomedical)
Fluorescence spectroscopy
Chemical composition
Diffraction
 Structural analysis
Focalisation = refractive lenses = Transfocator
• beam: mm down to less than 150 μm
• few % to 0.01 % spectral width with mono.)
• Flux ~ 1011 - 1013 ph/s
• 40 - 90 keV
• Flux ~ 108 - 1010 ph/s
• energy 40 - 90 keV
65 μrad
0.4 mm

## Slide 21: Preliminary analysis: characterization of the X-ray ThomX setup
Bravin1, P. Coan2, L. Franzoni1, F. Merighi1 and ThomX collaboration
1University Milano Bicocca (Milan, Italy)
2Ludwig Maximilians University (Munich, Germany)

## Slide 22
Assessment of the spatial resolution
Assessing the 10% MTF value is common method to evaluate the effective spatial resolution of an imaging system
MTF (modulation transfer function)
describes the system response to different spatial frequencies/various sizes
MTF value of 1 at low spatial frequencies ➔ low-frequency (large-scale) details are transferred with full contrast
Smaller MTF (as the spatial frequency increases) ➔ the system is less effective at reproducing finer details
Detector @ThomX: 13–14 line pairs per millimetre (lp/mm)
Should fulfil the requirement of resolving the blur generated @X-ray ThomX setup
First step: resolution of the taper optics Photonic Science detector

## Slide 23
Radiography: phase contrast imaging assessment
Wire/fishing line (propagation based) ~ 4,5m
Fishing line has only 1-2% absorption

## Slide 24
Sample: Bar Pattern
1000 projections from 0°to 180°
Next Steps:
Volume reconstruction and post-processing
First Computed Tomography (CT)
Technique for 3D Imaging
Phantom

## Slide 25
Recent measurements: Prostate biopsy
Prostate biopsy taken from patient exposed to metals

## Slide 26
ThomX is a research platform and demonstrator ! Different from commissioning/operation of a user facility.
X-ray flux of ~3  1010 ph/s is already demonstrated. Several working points available at 40 MeV, 50 MeV, 61.5 MeV and 70 MeV. Characterization of X-rays is in progress.
Currently one of the most advanced Compton source in operation: 1011 − 1012 ph/s expected in near future !
Recent cathode change (Mg): increase of the e- charge aiming for 1 nC (Mg photocathode) and operation at 50 Hz.
Fabry-Perrot cavity stored power gradually will be increased up to 500 kW. Goal: ~1012 ph/s
successful first X-ray experiments /commissioning : standard/phase contrast imaging, tomography, fluorescent spectroscopy … to be continued.
The help from SOLEIL’s team has been invaluable to us.
Summary
M. Alkadi, et al. "Commissioning of ThomX Compton source subsystems and demonstration of 1010 x-rays/s."
Phys. Rev. Accel. Beams 28 (2025): 023401

## Slide 27
Thank you!