## Slide 1
A low background setup for low energy X-ray detection
in the context of the BabyIAXO / IAXO axion searches
XDEP – X-ray DEtector
Technologies for Physics
5-6 February 2024 @ SOLEIL
M. Loidl, M. Rodrigues, M. Zahir, Q. Drenne

## Slide 2
The BabyIAXO / IAXO solar axion searches (1/2)
Axions:
Proposed as a solution of the strong CP problem of the standard model
Primordial axions would be a natural dark matter candidate
Search (in tunable microwave
cavities) extremely challenging
Axions should be copiously
produced in stellar cores,
e. g. in the sun
Discovery of axions
within a substantial
part of the relevant
parameter space
in reach for IAXO

## Slide 3
The BabyIAXO / IAXO solar axion searches (2/2)
IAXO:
Full-scale experiment with 8-bore magnet
Will be hosted at DESY
BabyIAXO:
Smaller 2-bore magnet
Fully funded, under construction
Experimental challenge: Low energy threshold (~ 0,5 keV), very low back-ground X-ray detectors

## Slide 4
Aim of the MMC test programme
Determine the intrinsic background of an MMC based X-ray detector array
Requirement: ~ 10-7 counts/keV/cm2/s (BabyIAXO)
~ 10-8 counts/keV/cm2/s (IAXO)
Actual level:
Shielding
Muon veto
Measured at KIP,
University of Heidelberg

## Slide 5
Dilution refrigerator @ LNHB (1/5)
inside
outside
Experimen-
tal space:
F = 92 mm
h = 300 mm
Liquid helium dewar
Dilution unit
Wired for 10 MMC & SQUID channels
Base temperature ~ 13 mK

## Slide 6
Dilution refrigerator @ LNHB (2/5)
External lead shielding
40 cm
60 cm
150 cm
10 cm Pb shield
324 lead bricks
~ 3.5 tons
98.8% solid angle coverage
Top: flexible lead mattes available
Experimental space
Flexible lead mattes

## Slide 8
Internal lead + copper shielding
Mixing chamber plate
Top internal lead
shielding: 2 cm
Side and bottom
internal lead
shielding: 5 mm
Side and bottom
internal copper
shielding: 3 mm
90 mm
200 mm
Top internal
copper mounting
& shielding plate:
5 mm
74 mm
Dilution refrigerator @ LNHB (4/5)

## Slide 9
Internal lead + copper shielding
~ 100 yrs old lead
210Pb: (2.27 ± 0.69) Bq/kg
CuC2 copper
Dilution refrigerator @ LNHB (5/5)

## Slide 10
Internal muon veto (1/2)
Ge wafer, 50.8 mm (2″) diam.,
1 mm thick
Atmospheric muons:
E deposit few 10s of keV
CGe = 48.5 pJ/K @ 20 mK;
Gold phonon collector films
4 x f 7 mm
CAu ≈ 41.4 pJ/K @ 20 mK
Gold wire bonds to MMC sensor
Cwires ≈ 4.0 pJ/K @ 20 mK
Cveto ≈ 94 pJ/K @ 20 mK
Expected count rate: ~ 0.5 s-1
One MMC, one SQUID channel
Copper
Ge wafer
~
>
PTFE
Gold phonon
collector films
MMC
SQUID

## Slide 11
Muon veto Ge wafer w/ Au phonon collector films
PTFE wafer holder pieces
Muon veto
MMC + SQUID
Internal muon veto (2/2)

## Slide 12
maXs-30 X-ray array
8 x 8 array, Au absorbers 500 x 500 µm2 each, 30 µm thickness
Full array surface area: 4 x 4 mm2
32 MMCs 32 SQUID channels required for full array readout
Expected DE ≈ 6 eV (FWHM)
Actual LNHB wiring: 1 quadrant can be read out 2 x 2 mm2
One chip received from KIP, Heidelberg University
X-ray detector: MMC chip options (1/5)

## Slide 13
Octagonal design to optimize match with cylindric absorbers, best suited for MetroBeta
Slight difference (5 %) in sensor area to create a net magnetization signal for temperature information
On-chip heat bath for sensor thermalization
Electroplated Au layer with high RRR on top of each sensor for fast heat diffusion over the entire sensor area, to avoid position dependences
Three sets of bondpads to match different experimental setups
on-chip
heat bath
thermal
link
bond pads
meander shaped
pick-up coil
sensor
heat
switch
MetroBeta/MetroMMC chips
X-ray detector: MMC chip options (2/5)

## Slide 14
Chip designation | XS | S | M | L | XL
Heat capacity Cabs @ 20mK | 8 pJ/K | 28 pJ/K | 110 pJ/K | 400 pJ/K | 1,7 nJ/K
SQUID type | PTB X1 | PTB X1 | PTB X1 | PTB XS | PTB S
Sensor area Asens (square) | (249 µm)2 | (335 µm)2 | (538 µm)2 | (1427 µm)2 | (2663 µm)2
Sensor height hsens | 3 µm | 3 µm | 3 µm | 3 µm | 3 µm
Energy resolution DEFWHM | 5.2 eV | 9.5 eV | 19.1 eV | 37.5 eV | 74.4 eV
Designed for nuclear decay data measurements within a wide energy range,
e. g. beta spectra with Qb ranging from few keV to ~ 1 MeV
5 sensor sizes to span a wide range of absorber heat capacities
MetroBeta/MetroMMC chips
X-ray detector: MMC chip options (3/5)

## Slide 15
MetroBeta/MetroMMC chips
Two absorbers 4.08 mm x 2.04 mm x 10 µm each
x 2 MMC chips 33.3 mm2 active area
400 pJ/K @ 10 mK
Actual choice
L size MMC
X-ray detector: MMC chip options (4/5)

## Slide 16
maXsIAXO
8 x 8 Au absorbers 1.25 x 1.25 mm2
Full array surface area: 1 cm2
10 µm thickness
Detection efficiency:
  > 99% up to 8 keV
  > 90% up to 10 keV
  Expected DE ≈ 11 eV (FWHM)
32 MMCs for full array
32 SQUID channels required
Actual LNHB wiring:
1 quadrant can be read out
5 x 5 mm2
Fabrication still pending …
X-ray detector: MMC chip options (5/5)

## Slide 17
Configuration for background measurement (1/3)
Collimators
55Fe sources
muon veto wafer
muon veto
MMC & SQUID
X-ray MMCs
& SQUIDs

## Slide 18
Muon veto
55Fe sources & collimators
X-ray MMCs
Configuration for background measurement (2/3)

## Slide 19
First test results (1/2)
One X-ray MMC (or its immediate surrounding) is contaminated: > 1 c/s
Second X-ray MMC: ~ 1 count / absorber / 5 min
Muon veto works: most pulses in the “clean” X-ray MMC are in coincidence with the veto.
Veto only count rate: ~ 1 count / 3 s
A few very low energy pulses in the X-ray MMC are not in coincidence with the veto
55Fe X-rays not identifiable no energy scale
Various problems with data acquisition
no exploitable spectra, no background rate

## Slide 20
First test results (1/2)

## Slide 21
Summary and outlook
External and internal shielding of the LNHB dilution refrigerator
  10 cm standard lead (external)
  5 mm low background lead (internal)
  3 mm low background copper (internal)
Muon veto: Ge wafer + Au films + Au bonding wires + MMC
Problems with
  Contamination (1/2 MMCs)
  55Fe sources
  Data acquisition
Next steps:
Replace brass screws by copper screws & standard solder by bonding from ribbon cables to MMC + SQUID chips
First figure of background level
Upgrade to 1 cm2 X-ray detector area

## Slide 22
Increase X-ray
detection area
3 X-ray detector layers
1 cm2 active area
3-4 veto layers
in total
9-10 MMC
& SQUID channels
Configuration for background measurement (3/3)

## Slide 23
Thank you for
your attention!