## Slide 1: Recent progress in PETRA IV orbit feedback design
11th "Diagnostics Experts of European Light Sources" (DEELS) workshop
Sven Pfeiffer for the WP2.08 team
Burak Dursun, Szymon Jablonski, Sajjad Hussain Mirza, Holger Schlarb, Jan Magnus Christmann (TU Darmstadt), …
Saint-Aubin, 10.06.2024

## Slide 2: FOFB system topology
Latency optimized topology
1 central control unit (GLO)
  Close to RF system / timing system
  Short path from GLO to LOC in experimental halls
15 distributed local sections (LOC)
  BPM collector
  Transmitter to power supplies
Optical fiber communication links
  Global to all local systems  classical regulation
  Local to local system
    For local control scheme integrating experiments
    Redundant system mode as future upgrade
Ring: 2.3km, 789 BPMs, 560 fast correctors, FOFB: 10% (5%, 3%) beam stability, DC to 1kHz

## Slide 3: FOFB System Design

## Slide 4: FOFB system: a cross-directional problem
The goal is to maintain the beam position throughout the ring → Spatial domain
Over time → Temporal domain
All corrector channels should have identical temporal response
A two dimensional control problem
  G(s) =
G(s) = G(s)R
C(s) = C(s)
with
2 step simulation
Dynamical system at 1 location with all TFs
  Worst case scenario  best case for MIMO
Spatial (MIMO) system with main dynamics

## Slide 5: FOFB system
Subsystems based on PETRA IV design
Disturbance spectra approximated with measurement at PIII
PI controller optimized for 1kHz disturbance rejection
Sensitivity function for disturbance rejection
Complementary S for reference tracking
SISO simulation
1Hz for 23mH
60kHz
7kHz
30kHz
1.5us
15us
7.5us
20.4us
23.1us
65kHz
0.167mm/A
zoh
40 & 50kHz
ISP
VSP
VD
ID
0.1um
BPM
(noise)
PI controller
Magnet Power Supply
(PWM as noise)
Plant: Magnet, vacuum chamber and ORM element
Disturbance
(based on PIII)
Loop delay ~ 75µs
Orbit in vacuum chamber

## Slide 6: PIV - FOFB system
Dynamic transfer functions
  Fast corrector magnet
    G = 1/(R + sL) (~Hz BW)
    Lamination thickness (30kHz - fractional order)
  Vacuum chamber (7kHz BW)
  Magnet power supply
    Output filter (30kHz)
  BPM electronics
Delays
  Processing delay
  Signal propagation
  Communication (time between sending and receiving)
Fast corrector magnet and vacuum chamber
Noise
  PS Quantization noise
  Pulse width modulation of the magnet power supply
  BPM electronic / sensor noise
Disturbances
  Incoherent: DC … kHz
Spatial disturbances
  Coherent: <1Hz (ocean waves)
  Transition: 1…10Hz (traffic noise)
2 step procedure
Simulation for optimization
  Started as Master thesis, now PhD thesis
Validation on test bench
  Corrector magnet including VC (and quads)
Institute for Accelerator Science and Electromagnetic Fields (TEMF)

## Slide 7: PIV - FOFB system
Dynamic transfer functions
  Fast corrector magnet
    G = 1/(R + sL) (~Hz BW)
    Lamination thickness (30kHz - fractional order)
  Vacuum chamber (7kHz BW)
  Magnet power supply
    Output filter (30kHz)
  BPM electronics
Delays
  Processing delay
  Signal propagation
  Communication (time between sending and receiving)
BPM electronics
Noise
  PS Quantization noise
  Pulse width modulation of the magnet power supply
  BPM electronic / sensor noise
Disturbances
  Incoherent: DC … kHz
Spatial disturbances
  Coherent: <1Hz (ocean waves)
  Transition: 1…10Hz (traffic noise)
Noise measured at PIII
Adapted for PIV simulation
IN
OUT
BPM noise as function of bunch pattern, … ?
Model for DDC (digital down conversion)

## Slide 8: PIV - FOFB system
Dynamic transfer functions
  Fast corrector magnet
    G = 1/(R + sL) (~Hz BW)
    Lamination thickness (30kHz - fractional order)
  Vacuum chamber (7kHz BW)
  Magnet power supply
    Output filter (30kHz)
  BPM electronics
Delays
  Processing delay
  Signal propagation
  Communication (time between sending and receiving)
Disturbance integration - SISO
Noise
  PS Quantization noise
  Pulse width modulation of the magnet power supply
  BPM electronic / sensor noise
Disturbances
  Incoherent: DC … kHz
Spatial disturbances
  Coherent: <1Hz (ocean waves)
  Transition: 1…10Hz (traffic noise)
BPM Measurement at PIII
Approximation for simulation
Start with PIII disturbance model to check PIV system simulations
 Expect reduced distortions at PIV by optimization of girder eigenfrequencies

## Slide 9: PIV - FOFB system
Dynamic transfer functions
  Fast corrector magnet
    G = 1/(R + sL) (~Hz BW)
    Lamination thickness (30kHz - fractional order)
  Vacuum chamber (7kHz BW)
  Magnet power supply
    Output filter (30kHz)
  BPM electronics
Delays
  Processing delay
  Signal propagation
  Communication (time between sending and receiving)
Blocks for simulation
Noise
  PS Quantization noise
  Pulse width modulation of the magnet power supply
  BPM electronic / sensor noise
Disturbances
  Incoherent: DC … kHz
Spatial disturbances
  Coherent: <1Hz (ocean waves)
  Transition: 1…10Hz (traffic noise)
MIMO simulation and mode space analysis

## Slide 10: SISO simulation

## Slide 11: FOFB system
Disturbance spectra approximated with measurement at PIII
Subsystems based on PETRA IV design
PI controller optimized for 1kHz disturbance rejection
150nm measured
132nm expected
 4…5% beam size
SISO simulation
Zoom in y
Factor 40 (32dB)
reduction by feedback;
Limited to FB controller and BPM noise
Red: measured with BPM noise
Blue: simulated without BPM noise
Waterbed effect increasing orbit jitter
(latency and dynamics dependent)

## Slide 12: Fractional order systems and it’s modelling

## Slide 13: Fractional order systems and it’s modelling
Yoke  next slides
SS vacuum chamber with symmetric CU transitions
Two potential system with fractional order characteristic
SS vacuum chamber with CU transition
First order approximation seems sufficient

## Slide 14: TEMF simulations
Yoke variations
1st prototype magnet with PowerCore 1400 and 1mm lamination
  3kHz with -10deg.
2nd prototype magnet with PowerCore 1400 and 0.3mm lamination
  30kHz with -10deg.

## Slide 15: Fractional order characteristics
First order system
All subsystems in full simulation approximated by first or higher order
  Assumption: worst case scenario with minimum phase margin in feedback
Modelling
Fractional order characteristics
First order fractional system
Fractional order systems
… is a dynamical system that can be modeled by a fractional differential equation containing derivatives of non-integer order (Wiki).

## Slide 16: SISO Fractional Order System Simulation

## Slide 17: Fractional order characteristics
PI controller for yoke lamination
PI controller with linear system  1st order modelling
PI controller with fractional order system  reality
PI controller adapted with fractional order system
Simulation
Dominating pole as approximation of the main plant characteristics (5kHz)
Feedback delay ~75us
Magnet laminations as
  Linear approximation
  Fractional order system
PI Feedback controller
  Designed with linear approximation
  Matched with fractional characteristics

## Slide 18: Fractional order characteristics
PID controller for yoke lamination
Simulation
Dominating pole as approximation of the main plant characteristics (5kHz)
Feedback delay ~75us
Magnet laminations as
  Linear approximation
  Fractional order system
PI Feedback controller
  Designed with linear approximation
  Matched with fractional characteristics
63% SS
500Hz mismatch in closed loop.
BUT with adopted PID settings similar reference tracking characteristic achieved.
I gain +10%
P gain +50%

## Slide 19: Fractional order characteristics
PID controller for yoke lamination
Simulation
Adapted PID settings for faster reference tracking at the beginning (first 0.1ms)
Mismatch of the low frequency tracking
Might not be relevant for disturbance suppression feedback
BUT, might be of importance for integration of photon diagnostics using reference tracking  longer settling time
Linear vs fractional order system:
>1ms to reach convergence

## Slide 20: Conclusion & Outlook
Models (few) derived for (most) PIV systems
Simulations of fast/slow corrector magnet, vacuum chamber by TEMF
BPM noise characteristics measured at PETRA III
  Partly open for charge/bunch pattern/ … variations
Disturbance spectra of PETRA III for PIV simulations
Fractional order modelling of laminations and effect to feedback regulation with adapted PI settings
  Observed larger convergence time for reference tracking
Outlook
Next: Validation of first prototype corrector on magnet test bench
MIMO simulations with disturbance models
  Coherence length, PSD, girder transfer characteristic…
…
Thank you

## Slide 21
Sven Pfeiffer
DESY - MSK
sven.pfeiffer@desy.de
+49 40 8998 2744